## Slide 1
TRIGENIX / PROJECT WALKTHROUGH
From image
to 3D model
How upload validation, image processing, reconstruction, and the viewer work
SOURCE WALKTHROUGH
Based on the current Trigenix project code
01
Notes: Overview of the actual Trigenix code path, from browser file selection through viewing and downloading the reconstructed model.

## Slide 2
TRIGENIX · IMAGE TO 3D
The complete processing flow
02
01 Select & inspect
02 Validate & save
03 Segment & prepare
04 Views & depth
05 Reconstruct mesh
06 Check, export & view
Browser
server.py
processor.py + pose_estimator.py
Zero123++ + Depth Anything
reconstructor.py
quality report + Three.js viewer
Key distinction: photo warnings run in the browser before upload; mesh printability checks run after reconstruction.
Notes: The deck follows this order. The photo quality heuristic is client-side and does not block upload. Server-side reconstruction quality is about the generated mesh.

## Slide 3
TRIGENIX · IMAGE TO 3D
01 File selection and MIME hints
03
The file picker’s accept attribute asks the browser to show image files.
Drag-and-drop and paste paths also check the browser-reported MIME type.
These are convenience filters. The backend still validates the upload.
<input type="file"
accept="image/*">
if (f && f.type.startsWith('image/')) {
_loadFile(f);
}
HTML/DropImage.html:329 · JS/DropImage.js:404–413
A filename or MIME label alone cannot prove what the bytes contain.
Notes: The file input accept attribute is a browser picker hint, not a security boundary. Picker selection calls _loadFile without checking MIME; drop and paste paths check type.startsWith("image/").

## Slide 4
TRIGENIX · IMAGE TO 3D
02 Browser-side photo checks
04
Canvas makes the image’s pixels available to JavaScript. The code shrinks large images to a maximum 200 px side, then calculates:
• Resolution: warn if either side < 256 px
• Luminance: 0.299R + 0.587G + 0.114B
• Mean brightness: warn below 40 or above 220
• Luminance variance: warn below 200
• Corner luminance range: warn above 80
• Non-white pixel fraction: warn below 5%
var canvas = document.createElement('canvas');
var scale = Math.min(1, 200 / Math.max(w, h));
canvas.width = Math.round(w * scale);
canvas.height = Math.round(h * scale);
var ctx = canvas.getContext('2d');
ctx.drawImage(img, 0, 0, canvas.width, canvas.height);
var data = ctx.getImageData(0, 0, canvas.width, canvas.height).data;
var avgBright = totalBright / n;
if (avgBright < 40) warnings.push('too dark');
JS/DropImage.js:268–345
These are warning heuristics, not a single score or an upload rejection.
Notes: Contrast variance and non-white fraction are approximations. This code does not implement a dedicated blur detector or semantic object detector.

## Slide 5
TRIGENIX · IMAGE TO 3D
03 Upload and server validation
05
Clicking Generate sends the File in multipart/form-data to POST /upload.
The server checks the request size, allowed filename suffix, and decoded image content before writing the upload to disk.
ALLOWED_IMAGE_EXTS = {
".png", ".jpg", ".jpeg", ".webp"
}
ext_in = os.path.splitext(filename_in)[1].lower()
if ext_in not in ALLOWED_IMAGE_EXTS:
raise ValueError("Unsupported image type")
with Image.open(io.BytesIO(data_in)) as img:
img.verify()
JS/DropImage.js:463–495 · server.py:14–16, 820–835
The server checks actual content with Pillow; extension and browser MIME are not enough.
Notes: The request body is parsed into item_data bytes. validate_image_payload checks byte size, extension, Pillow verify, then checks detected format against png/jpeg/webp.

## Slide 6
TRIGENIX · IMAGE TO 3D
04 UUID filename and upload storage
06
Only after validation succeeds, the server creates a UUID filename and writes the bytes into uploads/.
The user’s original name is not used as the disk filename. The validated suffix is kept.
ext = validate_image_payload(
item_filename, item_data
)
filename = str(uuid.uuid4()) + ext
filepath = os.path.join(UPLOAD_FOLDER, filename)
with open(filepath, "wb") as f:
f.write(item_data)
server.py:837–843
Validation → UUID name → write to uploads/ → image processing
Notes: UUIDs reduce collisions and avoid trusting a user-supplied path as the storage filename. The suffix is derived from the validated extension.

## Slide 7
TRIGENIX · IMAGE TO 3D
05 Background removal with rembg
07
The project loads the IS-Net general-use model. It estimates a foreground mask from learned visual patterns—shape, boundaries, and context. It does not use a fixed “not white = object” rule.
The estimate can be imperfect. If rembg raises an error, the code logs it and falls back to the original image.
def load_rembg():
from rembg import new_session
return new_session("isnet-general-use")
removed = remove(
white_bg, session=load_rembg()
)
processor.py:88–93, 212–225
The model predicts foreground pixels; it does not identify the object’s name.
Notes: IS-Net is a dichotomous image segmentation model. The project calls rembg with the isnet-general-use session and obtains an RGBA image with an alpha mask.

## Slide 8
TRIGENIX · IMAGE TO 3D
06 Clean the mask and crop the subject
08
The returned alpha channel becomes a binary mask at the default threshold 64/255.
Cleanup shrinks tiny specks, keeps only the largest connected component, expands/smooths the mask, and thresholds it again.
Then the code crops the foreground bounds, adds 12% padding, centers it in a square, and saves masked.png.
FG_ALPHA_THRESHOLD = int(
os.environ.get("TRIGENIX_FG_ALPHA_THRESHOLD", "64")
)
m = Image.fromarray((alpha_arr >= FG_ALPHA_THRESHOLD)
.astype(np.uint8) * 255, "L")
# keep largest connected region; expand + smooth
mask = _clean_mask(np.array(removed.split()[3]))
img_rgba = subject_crop(Image.merge("RGBA", (r,g,b,mask)))
img_rgba.save(f"{out_dir}/masked.png")
processor.py:32, 133–160, 212–226
The largest-component rule can also discard a real disconnected part of the object.
Notes: Mask cleanup applies Pillow min/max filters, connected-component labeling, Gaussian blur, and a threshold. Subject crop uses alpha bounds with pad_frac=0.12.

## Slide 9
TRIGENIX · IMAGE TO 3D
07 Estimate the object’s pose
09
The pose estimator reuses masked.png’s alpha mask. It measures the foreground silhouette to estimate orientation and framing.
PCA finds the major axis from foreground pixel coordinates. Left-right symmetry and the bounding box help estimate roll, azimuth, elevation, and distance.
This is a 2D silhouette-based estimate, not true 3D pose recovery.
pts_c = pts - pts.mean(axis=0)
cov = (pts_c.T @ pts_c) / len(pts_c)
eigvals, eigvecs = np.linalg.eigh(cov)
major = eigvecs[:, 1]
angle = np.degrees(np.arctan2(
major[1], major[0]
))
result.upright = aspect < 0.75
pose_estimator.py:63–74, 90–108
If pose estimation fails, the pipeline logs a warning and continues.
Notes: PCA uses covariance eigenvectors to infer the primary orientation of the foreground mask. Later formulas apply heuristic thresholds for roll/elevation/azimuth.

## Slide 10
TRIGENIX · IMAGE TO 3D
08 Generate views and estimate depth
10
With one photo, Zero123++ synthesizes six additional views. If the user provided six extra photos, the project prepares those instead.
Depth Anything estimates relative depth for the front image and views. These maps are useful visual outputs, but the current TripoSR geometry path does not consume them as calibrated depth.
grid = pipe(
img_in, num_inference_steps=25
).images[0]
front_rgb = img_rgba.convert("RGB").resize((320, 320))
all_images = [front_rgb] + [
v.resize((320, 320)) for v in views
]
estimate_depths(all_images, out_dir)
processor.py:309–354, 465–478
Synthesized views are AI predictions of unseen sides—not real photographs.
Notes: Depth Anything output is normalized per image and saved as grayscale/color PNGs. The reconstructor explicitly marks depth_maps false for geometry input, and notes relative depth is not used as metric depth.

## Slide 11
TRIGENIX · IMAGE TO 3D
09 Reconstruct a 3D shape
11
A background worker loads the masked front image and views, then selects an available backend.
In the TripoSR path, the model predicts a 3D representation from the masked front photo and extracts a triangle mesh. Generated views are used later for color repainting, not TripoSR shape geometry.
scene_codes = model([image], device=device)
meshes = model.extract_mesh(
scene_codes,
has_vertex_color=True,
resolution=res,
)
mesh = meshes[0]
reconstructor.py:2253–2270, 2621–2670
Mesh = vertices (3D points) + faces (triangles joining those points).
Notes: Auto mode can try InstantMesh if its required runtime dependencies are available, then TripoSR. The exact selected backend depends on runtime availability. TripoSR extracts at descending configured resolutions if a higher resolution fails.

## Slide 12
TRIGENIX · IMAGE TO 3D
10 Repair, orient, and check the mesh
12
The mesh is checked before and after cleanup. The cleanup keeps the largest component, repairs common defects, and may simplify meshes depending on the backend. Then the project orients and normalizes it.
Silhouette IoU compares a rendered silhouette against an input silhouette:
IoU = overlap area ÷ combined area
validate_mesh_topology(mesh, "A-raw")
mesh = cleanup(
mesh, keep_largest=True, ...
)
mesh = _orient_and_normalize(
mesh, out_dir, target_dimensions_mm
)
_sil_iou = _compute_silhouette_iou(mesh, views)
reconstructor.py:2299–2330
IoU is a silhouette fit measure; it cannot prove hidden geometry is correct.
Notes: The code logs IoU under 0.35 as low and under 0.10 as very low. It is diagnostic rather than a hard failure gate.

## Slide 13
TRIGENIX · IMAGE TO 3D
11 Quality report and file profiles
13
The project keeps a visual mesh and a print mesh. The visual version can preserve intentional openings; the print profile is intended for manufacturing.
Print-ready requires a watertight print mesh, one connected component, and at least 1,000 faces. If units are millimeters, the smallest dimension must meet the configured minimum (default 0.8 mm).
print_ready = bool(
print_mesh.is_watertight
and len(print_parts) == 1
and len(print_mesh.faces) >= 1000
)
if print_units == "millimeters" and min(print_dims.values()) < min_feature_mm:
print_ready = False
reconstructor.py:1922–1947
Exports can include GLB, STL, AR/VR, game, simulation, and other profiles.
Notes: Thresholds and findings are topology/printability checks, not image quality checks or a guarantee of printer success. The project returns profile URLs and a quality report.

## Slide 14
TRIGENIX · IMAGE TO 3D
12 Return the model to the browser
14
The upload response first returns views and depth maps and marks reconstruction as running. The browser polls /recon_status every five seconds.
When complete, the page shows mesh counts, dimensions, method, print status, quality issues, and links to view or download files. Generated file requests require authentication and ownership.
if (d.status === 'done' || d.status === 'success') {
_updateReconCard('done', d);
_updateCompareViewer(d.final_glb);
}
new THREE.GLTFLoader().load(blobUrl,
function(g) {
finishLoad(g.scene, name, 'GLB');
}
);
JS/DropImage.js:558–587 · HTML/Viewer3d.html:559–581
End state: inspect the model, download the GLB, or choose a print/export profile.
Notes: The viewer uses Three.js GLTFLoader to parse and render GLB. The server checks authentication, path safety, allowed generated extensions, and user ownership before serving generated assets.